## Slide 1: PIM Master™ – MW82119B Passive Intermodulation (PIM) Analyzer with Site Master™ Cable & Antenna Analyzer Option

## Slide 2: MW82119B – New 3rd Generation PIM Master™
Integrated Test Solution
  One instrument certifies both PIM and Sweep performance
  Fewer transit cases to carry to the site
  Fewer instruments to hoist to the top of tower
  Both test capabilities available when you need them
+
=
MW82119A
PIM Master™
S331E
Site Master™
MW82119B PIM Master™ with Option 331
NEW

## Slide 3: MW82119B – Features
PIM Analyzer test port: 7-16 DIN
Site Master test port: Type-N (Option 331)
Designed with separate test ports to maximize sweep test performance
  Highest accuracy
  Widest sweep bandwidth

## Slide 4: Site Master™ Cable & Antenna Analyzer (Option 331)
Measurements
  Return Loss, VSWR,
  Cable Loss
  Distance-to-Fault (DTF)
  1-port Phase
  Smith Chart
Performance expected from a Site Master™
  2 MHz to 3 GHz
  >42 dB directivity
  -4 dBm output power
  Interference immunity
Features expected from a Site Master™
  Dual screen display
  Quick-name matrix
  Flex Cal

## Slide 5: PIM Master™ Passive Intermodulation (PIM) Analyzer
Measurements
  PIM vs. Time
  Swept PIM
  Distance-to-PIM (DTP)
  Noise Floor
Frequency Options
  MW82119B-0700 – LTE 700 MHz (Upper & Lower)
  MW82119B-0702 – APT 700 MHz
  MW82119B-0800 – LTE 800 MHz
  MW82119B-0850 – Cellular 850 MHz
  MW82119B-0900 – E-GSM 900 MHz
  MW82119B-0180 – DCS 1800 MHz
  MW82119B-0194 – PCS/AWS 1900/2100 MHz
  MW82119B-0210 – UMTS 2100 MHz
  MW82119B-0260 – LTE 2600 MHz
Test power - 20 dBm (0.1 W) to 46 dBm (40 W)
NEW
NEW
NEW

## Slide 6: DTP / DTP Trace Overlay (existing capability)
  DTP / DTP overlay is an unique Anritsu PIM Master capability
  Use to identify PIM beyond the antenna
  Use to show “before” vs. “after” results
Distance between PIM marker & unknown PIM source
PIM marker DTP trace
Active DTP trace

## Slide 7: DTP / DTF Trace Overlay
Use higher resolution DTF measurements (Option 331) to help locate PIM
DTF into short clearly marks the end of feed cable
Here, the PIM is likely beyond the antenna
Cable end
NEW
DTF trace
Active DTP trace

## Slide 8: DTF / DTP Trace Overlay
DTF into precision load marks connector locations
Here, largest PIM is obviously at 2nd RF connection
Connector
Connector
Connector
DTF trace
Active DTP trace

## Slide 9: MW82119B – New features
Steel lifting rings for easy rigging
Access to screen & lifting rings in soft case
Stylus
(control wearing gloves)

## Slide 10: MW82119B – New features
Stronger tilt bail

## Slide 11: MW82119B – New Environmental tests
MIL-STD-810G
Transit Drop Test
48 in (1.2m) drop height
Each edge, corner, face
26 drops total
IP54 rating
Blowing dust
Water spray

## Slide 12
Questions?